## Slide 1: Exhaustive Directives Script
Brandon Greiner
SW Apps
19Mar2013
- Additional updates made 01Apr2014

## Slide 2: How did this come about?
When analyzing a CR, I started interacting with the CR Creator to get more information
At one point, the CR Creator asked if Vivado could do the same costing as ISE
  The answer was no, bit it gave me a great idea….
Great Idea:
  Why not have a Vivado script that calls all possible Implementation -directive combinations?
  Essentially this is doing a large number of strategies
  “Just launch it” when a customer escalation comes in
Maybe why this is a not-so-great idea:
  It might induce laziness, where instead of digging into timing problems where potentially the root cause is the design or XDC, the user will rely on throwing large number of switches to achieve closure

## Slide 3: Inputs
exhaustive_directives.tcl
An unimplemented DCP from synth_design or opt_design
Template Tcl Files
  place.tmpl.tcl
  phys_opt.tmpl.tcl
  route_opt.tmpl.tcl
Directive files
  monolithic_place_directives OR SSI_place_directives
  phys_opt_design_directives
  route_design_directives
Access to LSF

## Slide 4: Flow
postsynth.dcp*
phys_opt_design –directive <>
(optional)
place__design –directive <>
*Follows SRiTe QoR Naming Conventions
postphysopt.dcp
postplace.dcp*
route_design –directive <>
postroute.dcp*
wait
wait

## Slide 5: Flow Expansion
3 Route Directives
*Follows SRiTe QoR Naming Conventions
2 Phys_Opt Directives
(optional)
2 Place Directives
wait
wait
wait
wait
wait
wait

## Slide 6: Running the flow – configure exhaustive_directives.tcl
The top (header) of the script exhaustive_directives.tcl needs configured
# Set your LSF queue
set lsf_queue medium
##USE FOR SSI DEVICES## set lsf_queue long
# Set your LSF Project
set lsf_proj swapps_2013.x
# Set your estimated memory requirement for LSF in MB
# example: 4000 = 4GB
set lsf_mem 6000
# Do you want to run phys_opt_design directives?
# 0 = do not run phys_opt_design
# 1 = yes, run phys_opt_design directives
set run_phys_opt_design 1
# Set the opt_design or synth_design checkpoint here:
set dcp postlogicopt.dcp
# Set the place_design directive list here:
##USE FOR SSI DEVICES## set place_design_directive SSI_place_directives
set place_design_directive monolithic_place_directives
# Set the phys_opt_design directive list here:
set phys_opt_design_directive phys_opt_directives
# Set the route_design directive list here:
set route_design_directive route_directives
# The template file from which to do the switches
set tmplFile_place place.tmpl.tcl
set tmplFile_phys_opt phys_opt.tmpl.tcl
set tmplFile_route route.tmpl.tcl

## Slide 7: Running the flow – Template TCL Files
Template TCL Files contain several reserved keywords for the flow
  CHECKPOINT
  DIRECTORY
  PLACE_DIRECTIVE
  PLACE_CHECKPOINT
  PHYS_OPT_DIRECTIVE
  PREROUTE_CHECKPOINT
  ROUTE_DIRECTIVE
You can adjust Template TCL Files to provide more reports, etc.
  Just be certain to use the reserved keywords properly

## Slide 8: Running the flow – Directive files
Directive files contain the directives that the user would like to run
Monolithic Device
12 place directives
x 7 phys_opt directives
x 7 route directives
--------------------------------------------
588 route runs !!
SSI Device
17 place directives
x 7 phys_opt directives
x 7 route directives
--------------------------------------------
833 route runs !!
You can adjust Directive files to remove directives that do not need to be executed
Be aware, the number of combinations can be large
Monolithic Placement
Explore
WLDrivenBlockPlacement
LateBlockPlacement
ExtraNetDelay_high
ExtraNetDelay_medium
ExtraNetDelay_low
SpreadLogic_high
SpreadLogic_medium
SpreadLogic_low
ExtraPostPlacementOpt
RuntimeOptimized
Default
Phys Opt
Explore
AggressiveExplore
AlternateReplication
AggressiveFanoutOpt
AlternateDelayModeling
AddRetime
Default
Route
Explore
NoTimingRelaxation
MoreGlobalIterations
HigherDelayCost
AdvancedSkewModeling
RuntimeOptimized
Default
**Quick directives have been removed for place and route

## Slide 9: Running the flow – Execution Example
Script Directory: /proj/xcoswmktg/bgreine/exhaustive_directives_tcl
  Copy it into your area !!!
Command Line
  [bgreine@xcoswapps02 exhaustive_directives]$ ./exhaustive_directives.tcl | tee log
Output:
  Executing from Directory: /proj/xcoswmktg/bgreine/exhaustive_directives
  Design Checkpoint File: /proj/xcoswmktg/bgreine/exhaustive_directives/postlogicopt.dcp
  Place Design Directive File: /proj/xcoswmktg/bgreine/exhaustive_directives/monolithic_place_directives
  Phys Opt Design Directive File: /proj/xcoswmktg/bgreine/exhaustive_directives/phys_opt_directives
  Route Design Directive File: /proj/xcoswmktg/bgreine/exhaustive_directives/route_directives
  Place Template File: /proj/xcoswmktg/bgreine/exhaustive_directives/place.tmpl.tcl
  Phys Opt Design Directive File: /proj/xcoswmktg/bgreine/exhaustive_directives/phys_opt.tmpl.tcl
  Route Template File: /proj/xcoswmktg/bgreine/exhaustive_directives/route.tmpl.tcl
  Building Place Directive Data Structure:
  Explore
  WLDrivenBlockPlacement
  Building Phys Opt Directive Data Structure:
  Explore
  AggressiveExplore
  (Continued on next page)

## Slide 10: Running the flow – Execution Example (continued)
  Building Route Directive Data Structure:
  Explore
  NoTimingRelaxation
  MoreGlobalIterations
  HigherDelayCost
  Processing Place Directive: Explore
  Target Directory: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore
  Target TCL File: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore/Explore.tcl
  Target log File: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore/Explore.log
  Target jou File: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore/Explore.jou
  Target LSF Job Name: Explore
  Job submitted with ID: 333819
  Processing Place-Phys_Opt Directive Pair: Explore Explore
  Target Directory: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore.Explore
  Target TCL File: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore.Explore/Explore.Explore.tcl
  Target log File: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore/Explore.log
  Target jou File: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore.Explore/Explore.Explore.jou
  Target LSF Job Name: Explore.Explore
  Job submitted with ID: 333820
  Processing Place-Phys_Opt-Route Directive Combination: Explore Explore Explore
  Target Directory: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore.Explore.Explore
  Target TCL File: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore.Explore.Explore/Explore.Explore.Explore.tcl
  Target log File: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore/Explore.log
  Target jou File: /proj/xcoswmktg/bgreine/exhaustive_directives/Explore.Explore.Explore/Explore.Explore.Explore.jou
  Target LSF Job Name: Explore.Explore.Explore
  <lots more information>
  ##################################
  Tool processed 50 combinations
  ##################################

## Slide 11: Other Tips/Tricks
Use grep to get the results quickly
  egrep –A 6 “Design Timing Summary” */postroute.rpt | sort –u
  egrep -A 6 "Design Timing Summary" */post*.rpt | egrep -A 3 "WNS\(ns\)“ | sort -u
LSF Memory
  Know how much memory you need for your runs in advance and configure appropriately
LSF Queue
  Know how much runtime you need for a run
  Stick to medium queue
  Likely only SSI devices need the long queue (runtime > 8 hrs)
    Be aware that you are sometimes limited in the number of long queue jobs you can submit
Disk Space
  Do you have space for 500 runs at 300MB each?
    150GB
Unneccessary Directives
  Do you really need to run that particular directive?